## Slide 1: RSVP-TE
By-
Aditya Kusupati
Bharat
Aniruddha Kushwaha

## Slide 2: Outline
RSVP overview
RSVP-TE
Modification Over RSVP
Path Creation
Rerouting
Other Features
Comparison RSVP-TE CR-LDP

## Slide 3: RSVP Overview
The primary RSVP messages are PATH and RESV messages.
Senders send a PATH message from the source to the receiver to specify the reservation requirements of a data flow.
Receivers send a RESV message to the sender to reserve resources for the flow.
The primary object is the Session object, which identifies the data flow via the destination address, IP protocol ID, and destination port.
Other key objects include the Sender-Template and Sender-Tspec, which the switch uses to qualify the sender and traffic specification in the PATH message, and uses in the RESV message to further classify the flow, specify its resource requirements, and designate the reservation style.

## Slide 4: RSVP
Example shows a resource reservation for the {225.1.1.1, UDP, 1001} data

## Slide 5: RSVP
In addition to the PATH and RESV messages,
  RSVP also specifies support messages
    PATH-ERROR,
    RESV-ERROR,
    PATH-TEAR,
    RESV-TEAR, and
    RESV-CONFIRM
  That are used to handle error situations, to tear down existing reservations, and to confirm the setup of an existing reservation.

## Slide 6: RSVP-TE Overview
RSVP is a signaling protocol that reserves resources, such as for IP unicast and multicast flows, and requests quality-of-service (QoS) parameters for applications.
The protocol was extended RSVP TE for MPLS to enable RSVP to set up label switched paths (LSPs) in MPLS networks.
RSVP interacts with TE to support the MPLS TE functionality.

## Slide 7: RSVP-TE Overview
The TE process contains the following functionalities:
  End-point control, which is associated with establishing and managing TE tunnels at the headend and tailend.
  Link-management, which manages link resources to do resource-aware routing of TE LSPs and to program MPLS labels.
  Fast Reroute (FRR), which manages the LSPs that need protection and to assign backup tunnel information to these LSPs.

## Slide 8: Modification Over RSVP
RSVP TE builds on the RSVP core protocol, defines new objects, and modifies existing objects used in the PATH and RESV objects for LSP establishment.
The base Session construct for RSVP TE is based on the triplet
  {Tunnel Remote Address, Tunnel ID, Extended Tunnel ID}
Tunnel Remote Address
Reserved
Extended Tunnel ID
Tunnel ID
Extended Tunnel ID
A 32-bit identifier used in the SESSION that remains constant over the life of the tunnel.
Normally set to all zeros.
Ingress nodes that wish to narrow the scope of a SESSION to the ingress-egress pair may place their IPv4 address here as a globally unique identifier.

## Slide 9: Modification Over RSVP
The Sender Template object contains the
  {IPv4 tunnel sender address, LSP-ID}
Tunnel Sender Address
Reserved
LSP ID
LSP ID
A 16-bit identifier used in the SENDER_TEMPLATE and the FILTER_SPEC that can be changed to allow a sender to share resources with itself.

## Slide 10: Modification Over RSVP
The PATH message was extended to contain
  a Label-Request object (LRO) that results in a label being assigned during the RESV
  a Session-Attribute object that is used to provide additional requirements for a session, and
  an Explicit-Route object (ERO) that specifies the data path traversed by the PATH message.
The RESV message was modified to include
  a Label object that contains the MPLS label and
  a Record-Route object (RRO) to record the path taken followed by the RESV message.
The Flowspec object was also modified to set up a reservation on LSPs

## Slide 11: Modification Over RSVP
Explicit Route Object
  The contents of an EXPLICIT_ROUTE object are a series of variable length
  data items called subobjects.
Subobjects Content
Length
Type
L
  L bit -
  0 -> Strict Hop
  1 -> Loose Hop
  Type –
The Type indicates the type of contents of the subobject.
Currently defined values are:
1 -> IPv4 prefix
2 -> IPv6 prefix
32 -> Autonomous system number
Length -
The Length contains the total length of the subobject in bytes, including the L, Type and Length fields. The Length MUST be at least 4, and MUST be a multiple of 4
Subobject

## Slide 12: Path Creation
Creation by exchanging messages
  Two phases to the establishment of an LSP
    Phase 1: Sending a Message Path
    Phase 2: Sending a Resv message
Source
Destination
Path ; ER(ABC) ; LSP 1
A
B
C
Resv ; ER(CBA) ; LB = 20 ; LSP 1
Src | Dst
20 | 10
Resv ; ER(CBA) ; LB = 10 ; LSP 1
D

## Slide 13: Rerouting
"Make before break"
  1: Establishment of a new LSP
  2: Traffic Switch
  3: Destruction of the old LSP
Booking type SE: Shared Explicit
A
B
C
D
E
Tunnel 1
Tunnel 2
Creation of the second tunnel
  Identical SESSION
  ID different LSP
  Shared Explicit

## Slide 14: Other features
Detection loop
  Uses RRO
Detection of the MTU

## Slide 15: Comparison RSVP-TE CR-LDP
 | RSVP-TE | CR-LDP
Transport layer | Uses UDP or IP (raw IP) for the distribution of labels. | Uses TCP to distribute labels and UDP to discover the LSR
Protocol type | Soft-state protocol, requiring periodic refresh | Protocol-state hard.
Notifications | Provides a notification in case of failure. | Does not provide notification in case of failure.
Routing | explicit routing | explicit routing

## Slide 16: Thank You